## Slide 1
Accelerator-only ASIC Architecture
4 lanes • 64 vectors / bank • Digital core: stream_mmio
CORE OVERVIEW
Host Ports
32-bit
MMIO
Decoder
Configuration
W1/B1 • W2/B2
Command FIFO
4 entries
Job FSM
Bank • Layer • Tag
Status / Counters
Done • Error
≥1
IRQ
done[1:0]
Input RAM A/B
2 × 64 × 4 × 32
MUX
MAC Unit ×4
INT8 dot products
MUX
Adaptive Activation
4 lanes + 1 reference
Route
Result RAM A/B
2 × 64 × 4 × 32
Bank / Hidden
MAC / Direct
Direct: 4 × 19-bit
Q14 → Q7 / Clamp / Hidden RAM 64 × 32
Layer 1: tanh Layer 2: sigmoid Fixed-14
16-bit results, sign-extended
MAC DETAIL: ONE OUTPUT LANE ×4
16 signed multipliers total • 4 pipeline stages
x0 × w0
8-bit × 8-bit
×
x1 × w1
8-bit × 8-bit
×
x2 × w2
8-bit × 8-bit
×
x3 × w3
8-bit × 8-bit
×
Product registers: 4 × 16-bit
+
+
Pair registers: 2 × 17-bit
+
Bias
32-bit
Sum
34-bit
Round / Shift
19-bit Clamp
II = 1 when unstalled • Bias / shift / tag pipeline
ACTIVATION DETAIL: EARLY ×4 / SHARED FULL ×1
Magnitude bin / Iteration LUT
Sample mask / Lane MUX 0–3
Early CORDIC ×4
Budget iterations
Shared CORDIC ×1
Full iterations
Early / Tag
Full / Lane tag
|Early − Full| > T
&
Sample
MUX
Early
Full
Result: 16-bit
LUT update / Fallback counters
Mode: tanh / sigmoid / ReLU / linear
CORDIC PIPELINE
Range
reduce
16 shift-add
stages
y ÷ x
3× reconstruction
Mode / Saturation
Solid: data Dashed blue: control Register triangle: clock ≥1: OR &: AND
Digital-core architecture • Physical I/O, pads and SCL180 memory mapping pending • clk / rst_n omitted for clarity